## Slide 1: MODULE-2 Addressing Modes

## Slide 2: Generating Memory Addresses
How to specify the address of branch target?
Can we give the memory operand address directly in a single Add instruction in the loop?
Use a register to hold the address of NUM1; then increment by 4 on each pass through the loop.

## Slide 3: Addressing Modes
The way in which the location of an operand is specified in an instruction is called addressing mode.

## Slide 4: Addressing Modes..

## Slide 5: Addressing Modes..
Immediate mode
  The operand is given explicitly in the instruction.
    Move #200,R0
    Add #10,R1
Register mode
  The operand is the contents of a processor register; the name (address) of the register is given in the instruction.
    Move R1,R2
    Add R0,R1

## Slide 6: Addressing Modes..
Absolute mode (Direct mode)
  The operand is in a memory location; the address of this location is given explicitly in the instruction.
    Move LOC,R1
    Add A,R0
Indirect mode
  The effective address of the operand is the contents of a register or memory location whose address appears in the instruction.
    Move (R0),R1
    Add (LOC),R2

## Slide 7: Addressing Modes..

## Slide 8: Addressing Modes..

## Slide 9: Addressing Modes..
Index mode
  The effective address of the operand is generated by adding a constant value to the contents of a register.
  We indicate the Index mode symbolically as X(Ri)
  X(Ri): EA = [Ri]+X

## Slide 10: Addressing Modes..
The value X defines an offset (also called a displacement) from this address to the location where the operand is found.
  Move 20(R0),R1
  Add 1000(R1),R2
The constant X may be given either as an explicit number or as a symbolic name representing a numerical value.
If X is shorter than a word, sign-extension is needed.

## Slide 11: Addressing Modes..

## Slide 12: Addressing Modes..
Consider a simple example involving a list of test scores for students taking a given course.
A four-word memory block comprises a record that stores the relevant information for each student.
Each record consists of the student's identification number (ID), followed by the scores the student earned on three tests.

## Slide 13: Addressing Modes..

## Slide 14: Addressing Modes..
Suppose that we wish to compute the sum of all scores obtained on each of the tests and store these three sums in memory locations SUMI, SUM2, and SUM3.

## Slide 15: Addressing Modes..

## Slide 16: Addressing Modes..
Base with Index mode
  The effective address is the sum of the contents of registers specified in the instruction.
  (Ri,Rj): EA = [Ri]+[Rj]
    Move (R0,R1),R2
    Add (R1,R2),R0

## Slide 17: Addressing Modes..
Base with Index and Offset mode
  The effective address is the sum of the constant X and the contents of registers specified in the instruction.
  X(Ri,Rj): EA = [Ri]+[Rj]+X
    Move 20(R0,R1),R2
    Add 1000(R1,R2),R0

## Slide 18: Addressing Modes..
Relative mode
  The effective address is determined by the Index mode using the program counter in place of the general-purpose register Ri.
    Branch>0 LOOP
  X(PC) : EA = [PC] + X
  – note that X is a signed number
  This location is computed by specifying it as an offset from
the current value of PC.
  Branch target may be either before or after the branch instruction, the offset is given as a singed num.

## Slide 19: Addressing Modes..
Autoincrement mode
  The effective address of the operand is the contents of a register specified in the instruction.
  After accessing the operand, the contents of this register are automatically incremented to point to the next item in a list.
    Add (R2)+,R0
  The increment is 1 for byte-sized operands, 2 for 16-bit operands, and 4 for 32-bit operands.

## Slide 20: Addressing Modes..
Go to Figure 2.25

## Slide 21: Addressing Modes..
Autodecrement mode
  The contents of a register specified in the instruction are first automatically decremented and are then used as the effective address of the operand.
    Add -(R2),R0
  The decrement is 1 for byte-sized operands, 2 for 16- bit operands, and 4 for 32-bit operands.

## Slide 22: Assembly Language

## Slide 23: Assembly Language
Machine instructions are represented by patterns of 0s and 1s.
  Awkward to deal with when discussing or preparing programs.
  We use symbolic names
Assembly language – A complete set of symbolic names and rules for their use
Syntax - The set of rules for using the mnemonics in the specification of complete instructions and programs
Mnemonics

## Slide 24: Assembly Language..
Assembler – A program which translates programs written in an assembly language into a sequence of machine instructions
Source program - The user program in its original alphanumeric text format
Object program - The assembled machine language program

## Slide 25: Assembly Language..
MOVE R0,SUM
The mnemonic MOVE represents the binary pattern, or OP code (Operation Code)
R0 is Source operand and SUM is destination operand

## Slide 26: Assembly Language..
The assembly language must indicate which mode is being used.
For example
  A numerical value or a name used by itself, such as SUM in the preceding instruction, may be used to denote the Absolute mode.
  The sharp sign usually denotes an immediate operand.
    ADD #5,R3

## Slide 27: Assembly Language..
In some assembly languages, the intended addressing mode is indicated in the OP-code mnemonic.
In this case, a given instruction has different OP- code mnemonics for different addressing modes.
  ADDI 5,R3
Indirect addressing is usually specified by putting parentheses around the name or symbol denoting the pointer to the operand.
  MOVE #5,(R2)
  MOVEI 5,(R2)

## Slide 28: Assembler Directives
These are commands used by the assembler while it translates a source program into an object program.
  SUM EQU 200

## Slide 29: Assembler Directives..

## Slide 30: Assembler Directives..
To produce an object program, an assembler has to know
  How to interpret the names
  Where to place the instructions in the memory
  Where to place the data operands in the memory

## Slide 31: Assembler Directives..

## Slide 32: Assembler Directives..
EQU (equate) - informs the assembler that the variable name should be replaced by the value specified.
  In this case, SUM should be replaced by the value 200 wherever it appears in the program
ORIGIN - tells the assembler program where in the memory to place the data block that follows.
  In this case, the location specified has the address 204

## Slide 33: Assembler Directives..
DATAWORD - informs the assembler that the data value specified is to be placed in the memory word
  In this case, the data value 100 is to be placed in the memory word at address 204.

## Slide 34: Assembler Directives..
Any statement that results in instructions or data being placed in a memory location may be given a memory address label.
The label is assigned a value equal to the address of that location.

## Slide 35: Assembler Directives..
RESERVE - declares that a memory block of specified bytes is to be reserved for data
  In this case, a memory block of 400 bytes is to be reserved for data, and that the name NUM1 is to be associated with address 208.
END - tells the assembler that this is the end of the source program text.

## Slide 36: Assembler Directives..
Most assembly languages require statements in a source program
to be written in the form
Label Operation Operand(s) Comment
The Label is an optional name associated with the memory address
  Address of machine instructions
  Addresses of data items
The Operation field contains the OP-code mnemonic of the desired instruction or assembler directive.
The Operand field contains addressing information for accessing
one or more operands, depending on the type of instruction.
The Comment field is ignored by the assembler program.
  Used for documentation purposes
  Makes the program easier to understand.

## Slide 37: Assembly and Execution of Programs
A source program written in an assembly language must be assembled into a machine language object program before it can be executed.
  This is done by the assembler program
Assembler replaces all symbols denoting operations and addressing modes with the binary codes used in machine instructions, and replaces all names and labels with their actual values.

## Slide 38: Assembly and Execution of Programs..
A key part of the assembly process is determining the values that replace the names.
  Easy in some cases
  Branch offset
As the assembler scans through a source program, it keeps track of all names and the numerical values that correspond to them in a symbol table.
  When a name appears a second time, it is replaced with its value from the table.

## Slide 39: Assembly and Execution of Programs..
Two-pass assembler
  During the first pass, it creates a complete symbol table. At the end of this pass, all names will have been assigned numerical values.
  The assembler then goes through the source program a second time and substitutes values for all names from the symbol table.

## Slide 40: Assembly and Execution of Programs..
The assembler stores the object program on a magnetic disk.
The object program must be loaded into the memory of the computer before it is executed.
A utility program called a loader is used to load the object program into memory.

## Slide 41: Assembly and Execution of Programs..
The assembler can detect and report syntax errors.
Debugger program helps the user find other programming errors, the system software
  This program enables the user to stop execution of the object program at some points of interest and to examine the contents of various processor registers and memory locations.

## Slide 42: Number Notation
It is often convenient to use the familiar decimal notation.
  ADD #93,R1
  These values are stored in the computer as binary numbers.
In some situations, it is more convenient to specify the binary patterns directly.
  ADD #%01011101,R1
Binary numbers can be written more compactly as hexadecimal, or hex, numbers
  ADD #$5D,R1

## Slide 43: Basic Input/Output Operations

## Slide 44: I/O
The data on which the instructions operate are not necessarily already stored in memory.
Data need to be transferred between processor and outside world (disk, keyboard, etc.)
I/O operations are essential, the way they are performed can have a significant effect on the performance of the computer.

## Slide 45: Program-Controlled I/O Example
Consider a task that reads in character input from a keyboard and produces character output on a display screen.
  Rate of data transfer (keyboard, display, processor)
    Limited by the typing speed of the user
  The rate of output transfers from the computer to the display is much higher.
    Determined by the rate at which characters can be transmitted over the link between the computer and the display device
  Difference in speed between processor and I/O device creates the need for mechanisms to synchronize the transfer of data.

## Slide 46: Program-Controlled I/O Example..
A solution:
On output, the processor sends the first character and then waits for a signal from the display that the character has been received.
It then sends the second character.
Input is sent from the keyboard in a similar way.
  The processor waits for a signal indicating that a character key has been struck and that its code is available in some buffer register associated with the keyboard.
  Then the processor proceeds to read that code.

## Slide 47: Program-Controlled I/O Example..
Registers
Flags
Device interface
DATAIN
DATAOUT
SIN
K eyboard
SOUT
Display
Bus
Figure 2.19 Bus connection for processor, keyboard, and display.
Processor

## Slide 48: Program-Controlled I/O Example..
The keyboard and the display are separate devices as shown in Figure 2.19.
The action of striking a key on the keyboard does not automatically cause the corresponding character to be displayed on the screen.
One block of instructions in the I/O program transfers the character into the processor, and another associated block of instructions causes the character to be displayed.

## Slide 49: Moving a character code from the keyboard to the processor
Striking a key stores the corresponding
character code in an 8-bit buffer register DATAIN.
To inform the processor that a valid character is in DATAIN, a status control flag, SIN, is set to 1.
A program monitors SIN, and when SIN is set to 1, the processor reads the contents of DATAIN.
When the character is transferred to the processor, SIN is automatically cleared to 0.
If a second character is entered at the keyboard, SIN is again set to 1 and the process repeats.

## Slide 50: Transferring a character from the processor to the display
A buffer register, DATAOUT, and a status control flag, SOUT, are used for this transfer.
When SOUT equals 1, the display is ready to receive a character.
Under program control, the processor monitors SOUT, and when SOUT is set to 1, the processor transfers a character code to DATAOUT.
The transfer of a character to DATAOUT clears SOUT to
0.
When the display device is ready to receive a second character, SOUT is again set to 1.

## Slide 51: Program-Controlled I/O Example..
The buffer registers DATAIN and DATAOUT and the status flags SIN and SOUT are part of circuitry commonly known as a device interface.

## Slide 52: Program-Controlled I/O Example..
Machine instructions that can check the state of the status flags and transfer data between the processor and the I/O device. :
READWAIT Branch to READWAIT if SIN = 0
Input from DATAIN to R1
WRITEWAIT Branch to WRITEWAIT if SOUT = 0
Output from R1 to DATAOUT

## Slide 53: Program-Controlled I/O Example..
Memory-Mapped I/O – some memory address values are used to refer to peripheral device buffer registers.
  No special instructions are needed.
  Also use device status registers.
MoveByte DATAlN,R1
MoveByte R1,DATAOUT

## Slide 54: Program-Controlled I/O Example..
Let us assume that bit b3 in registers INSTATUS and OUTSTATUS corresponds to SIN and SOUT, respectively.
The read operation may be implemented by the machine instruction sequence
READWAIT Testbit #3, INSTATUS
Branch=0 READWAIT MoveByte DATAIN, R1
The write operation may be implemented as
WRITEWAIT Testbit #3, OUTSTATUS
Branch=0 WRITEWAIT
MoveByte R1,DATAOUT

## Slide 55: Program-Controlled I/O Example..

## Slide 56: Program-Controlled I/O Example..
Assumption – the initial state of SIN is 0 and the initial state of SOUT is 1.
Any drawback of this mechanism in terms of efficiency?
  Two wait loopsprocessor execution time is wasted
Alternate solution?
  Interrupt

## Slide 57: Stacks and Queues

## Slide 58: Stacks
A stack is a list of data elements, usually words or bytes, with the accessing restriction that elements can be added or removed at one end of the list only.
  This end is called the top of the stack, and the other end is called the bottom.
The structure is sometimes referred to as a pushdown stack.
Last-In-First-Out (LIFO) stack - the last data item placed on the stack is the first one removed when retrieval begins.
The terms push and pop are used to describe placing a new item on the stack and removing the top item from the stack, respectively.

## Slide 59: Stacks..
Assume that the first element is placed in location BOTTOM, and when new elements are pushed onto the stack, they are placed in successively lower address locations.
Figure 2.21 shows a stack of word data items in the memory of a computer.
It contains numerical values, with 43 at the bottom and -28 at the top.
Stack pointer (SP) - A register used to keep track of the address of the element of the stack that is at the top at any given time.

## Slide 60: Stacks..

## Slide 61: Stacks..
Assuming 32-bit word length, the PUSH operation will decrement the stack pointer by 4 and copies the source into the stack.
Can be implemented as
Subtract #4,SP
Move NEWITEM,(SP)
Or using autodecrement mode as
Move NEWITEM,-(SP)

## Slide 62: Stacks..
Assuming 32-bit word length, the POP operation will copy the content from the stack to the destination and increment the stack pointer by 4.
Can be implemented as
Move (SP),ITEM Add #4,SP
Or using autoincrement mode as
Move (SP)+,ITEM

## Slide 63: Stacks..

## Slide 64: Stacks..
Stack is usually allocated a fixed amount of space in the memory.
We must avoid pushing an item on a full stack and popping an item from an empty stack.
  Could result from a programming error.
Suppose that a stack runs from location 2000 (BOTTOM) down to 1500.
The stack pointer is loaded initially with address value 2004.

## Slide 65: Stacks..

## Slide 66: Stacks..
The Compare instruction
Compare src,dst performs the operation
[dst] - [src]
and sets the condition code flags according to the result.
It does not change the value of either operand.

## Slide 67: Queues
A queue is a list of data elements that works on first-in-first-out (FIFO) basis.
Data are stored in and retrieved from a queue on a first-in-first-out (FIFO) basis.
If we assume that the queue grows in the direction of increasing addresses in the memory, new data are added at the back (high-address end) and retrieved from the front (low-address end) of the queue.

## Slide 68: Differences between Stacks and Queues
Stacks | Queues
One end of the stack is fixed (the bottom), while the other end rises and falls as data are pushed and popped. | Both ends of a queue move to higher addresses as data are added at the back and removed from the front.
A single pointer is needed to point to the top of the stack at any given time. | Two pointers are needed to keep track of the two ends of the queue.
A stack is limited by the top and bottom of the stack in the memory. | A queue would continuously move through the memory of a computer in the direction of higher addresses.

## Slide 69: Queues..
One way to limit the queue to a fixed region in memory is to use a circular buffer.
Let us assume that memory addresses from BEGINNING to END are assigned to the queue.
  The first entry in the queue is entered into location BEGINNING, and successive entries are appended to the queue by entering them at successively higher addresses.
  By the time the back of the queue reaches END, space will have been created at the beginning if some items have been removed from the queue.
  Hence, the back pointer is reset to the value BEGINNING and the process continues.

## Slide 70: Subroutines
In a given program, it is often necessary to perform a particular subtask many times on different data values.
Such a subtask is usually called a subroutine.
For example, a subroutine may evaluate the sine function or sort a list of values into increasing or decreasing order.

## Slide 71: Subroutines..
To save space, only one copy of the instructions of the subroutine is placed in the memory, and any program that requires the use of the subroutine simply branches to its starting location.
When a program branches to a subroutine, we say that it is calling the subroutine.
The instruction that performs this branch operation is named a Call instruction.

## Slide 72: Subroutines..
After a subroutine has been executed, the calling program must resume execution, continuing immediately after the instruction that called the subroutine.
The subroutine is said to return to the program that called it by executing a Return instruction.

## Slide 73: Subroutines..
While a subroutine is called, provision must be made for returning to the appropriate location.
The location where the calling program resumes execution is the location pointed to by the updated PC while the Call instruction is being executed.
Hence, the contents of the PC must be saved by the Call instruction to enable correct return to the calling program.

## Slide 74: Subroutines..
Subroutine linkage method - The way in which a computer makes it possible to call and return from subroutines.
Simplest method - save the return address in a specific location, which may be a register dedicated to this function.
  Such a register is called the link register.
When the subroutine completes its task, the Return instruction returns to the calling program by branching indirectly through the link register.

## Slide 75: Subroutines..
The Call instruction is a special branch instruction that performs the following operations:
  Store the contents of the PC in the link register
  Branch to the target address specified by the instruction
The Return instruction is a special branch instruction that performs the operation:
  Branch to the address contained in the link register

## Slide 76: Subroutines..

## Slide 77: Subroutine Nesting and the Processor Stack
Subroutine nesting – subroutine calling another subroutine
In this case, the return address of the second call is also stored in the link register, destroying its previous contents.
  The contents of the link register has to be saved in some other location before calling another subroutine.
  Otherwise, the return address of the first subroutine will be lost.

## Slide 78: Subroutine Nesting and the Processor Stack..
Subroutine nesting can be carried out to any depth.
Eventually, the last subroutine called, completes its computations and returns to the subroutine that called it.
The return address needed for this first return is the last one generated in the nested call sequence.
That is, return addresses are generated and used in a last-in-first-out order.

## Slide 79: Subroutine Nesting and the Processor Stack..
The return addresses associated with subroutine calls should be pushed onto a stack.
  Many processors do this automatically as one of the operations performed by the Call instruction.
A particular register is designated as the stack pointer, SP, to be used in this operation.
  The stack pointer points to a stack called the
processor stack.

## Slide 80: Subroutine Nesting and the Processor Stack..
The Call instruction pushes the contents of the PC onto the processor stack and loads the subroutine address into the PC.
The Return instruction pops the return address from the processor stack into the PC.

## Slide 81: Parameter Passing
Parameter passing - The exchange of information between a calling program and a subroutine.
When calling a subroutine, a program must provide to the subroutine the parameters, that is, the operands or their addresses, to be used in the computation.
Later, the subroutine returns other parameters, in this case, the results of the computation.

## Slide 82: Parameter Passing..
The parameters may be placed in registers or in memory locations, where they can be accessed by the subroutine.
Alternatively, the parameters may be placed on the processor stack used for saving the return address.

## Slide 83: Parameter Passing..
Refer Figure 2.16

## Slide 84: Parameter Passing..
Figure 2.25 shows how the program in Figure
2.16 for adding a list of numbers can be implemented as a subroutine, with the parameters passed through registers.
The size of the list, n, contained in memory location N, and the address, NUM1, of the first number, are passed through registers R1 and R2.
The sum computed by the subroutine is passed back to the calling program through register R0.

## Slide 85: Parameter Passing..
If many parameters are involved, there may not be enough general-purpose registers available for passing them to the subroutine.
Using a stack, on the other hand, is highly flexible
  A stack can handle a large number of parameters.

## Slide 86: Parameter Passing..

## Slide 87: Parameter Passing by Value and by Reference
Note the nature of the two parameters, NUM1 and n, passed to the subroutines in previous examples.
Instead of passing the actual list entries, the calling program passes the address of the first number in the list.
  This technique is called passing by reference.
In case of the second parameter, the actual number of entries, n, is passed to the subroutine.
  This technique is called passing by value.

## Slide 88: Additional Instructions

## Slide 89: Logic Instructions
Logic operations such as AND, OR, and NOT, applied to individual bits, are the basic building blocks of digital circuits.
Bitwise logic instructions
  Not dst
  And src,dst
  Or src,dst

## Slide 90: Logic Instructions..
To find negative (2’s complement) of a number
Not R0 Add #1,R0
Many computers have a single instruction for this
Negate R0

## Slide 91: Logic Instructions..
Suppose that four ASCII characters are contained in the 32-bit register R0.
In some task, we wish to determine if the leftmost character is Z.
If it is, a conditional branch to YES is to be made.
The ASCII code for Z is 01011010, which is expressed in hexadecimal notation as 5A.

## Slide 92: Logic Instructions..
The three-instruction sequence implements the desired action.
And #$FF000000,R0
Compare #$5A000000,R0 Branch=0 YES
The And instruction is often used in practical programming tasks where all bits of an operand except for some specified field are to be cleared to 0.

## Slide 93: Shift and Rotate Instructions
Shift Instructions
  Logical Shift
  Arithmetic Shift
Rotate Instructions

## Slide 94: Logical Shifts
Logical shift
  Logical shift left (LShiftL)
  Logical shift right (LShiftR)
These instructions shift an operand over a number of bit positions specified in a count operand contained in the instruction.
General form
LShiftL count,dst LShiftR count,dst
The count operand may be an immediate operand, or it may be contained in a processor register.

## Slide 95: Logical Shifts..

## Slide 96: Arithmetic Shifts
Retains the sign of the number

## Slide 97: Arithmetic Shifts
Note:
  Shifting a number one bit position to the left is equivalent to multiplying it by 2; and shifting it to the right is equivalent to dividing it by 2.

## Slide 98: Rotate Operations
In the shift operations, the bits shifted out of the operand are lost, except for the last bit shifted out which is retained in the Carry flag C.
To preserve all bits, a set of rotate instructions can be used.
They move the bits that are shifted out of one end of the operand back into the other end.
Rotate without carry
Rotate with carry

## Slide 99: Rotate Operations..

## Slide 100: Rotate Operations..

## Slide 101: Digit-Packing Example
Suppose that two decimal digits represented in ASCII code are located in memory at byte locations LOC and LOC + 1.
We wish to represent each of these digits in the 4-bit BCD code and store both of them in a single byte location PACKED.
  The result is said to be in packed-BCD format.
Hence, the required task is to extract the low- order four bits in LOC and LOC + 1 and concatenate them into the single byte at PACKED.

## Slide 102: Digit-Packing Example

## Slide 103: Multiplication and Division
Not very popular (especially division)
Multiply Ri, Rj Rj ← [Ri] х [Rj]
2n-bit product case: high-order half in R(j+1)
Divide Ri, Rj Rj ← [Ri] / [Rj]
Quotient is in Rj, remainder may be placed in R(j+1)